## Slide 1
Project Title: | Study of Anti-fogging Coating using Powder Physical Vapour Deposition for Eyeglasses Application
Synopsis: | Fogging on eyeglasses can be a nuisance and arise safety issue to the wearer. Superhydrophilic coating has been widely used to provide antifogging property to optical glasses. This project aims to develop an anti-fogging coating of TiO2/Si3N4 using powder physical vapour deposition (PPVD) technique. TiO2 coating has been found to show superhydrophilicity after annealing process. Annealing on ceramic has often associated with cracking. The coating deposition by PPVD allows addition of several powder elements for coating to form uniform ultrathin layer. Here, addition of Si3N4 to conventional TiO2 coating may provide great anti-fogging strategy with good mechanical properties without the need of annealing.
Objectives: | To fabricate TiO2/Si3N4 ultra thin layer using PPVD with a set of parameters range To characterize resulting coating in terms of structure and its properties
Equipment required: | PPVD set-up, FESEM, AFM, contact angle, UV-Vis Spectroscopy, thermogravimetry,etc.
Software required: | Nil
Supervisor (Department): | AP Datin Ir. Dr. Bushroa Abdul Razak (Dept of Mechanical Eng.)
Program: | Master of Mechanical Engineering (Manufacturing Process)
Duration: | Maximum 2 consecutive semesters

## Slide 2
Project Title: | Study on the uniformity of TiO2 Nanotubes growth via Plasma Electrolytic Oxidation (PEO) Technique
Synopsis: | Titanium alloys (Ti6Al4V) have been receiving a lot of attention for medical implant applications due to their corrosion resistance, lightweight, biocompatibility, and mechanical strength. Surface modification of Ti6Al4V is frequently investigated to acquire the needed properties to produce better-performing medical devices. According to the literature, the development of passive TiO2 film can provide desired biocompatibility and inertness in titanium alloy implants. Researchers have been focused on improving the osseointegration properties as well as mechanical characteristics through nanostructured coatings. Nanostructured films are preferred over micro-sized films due to their superior corrosion resistance and biocompatibility. Over time, nanostructured TiO2 has been investigated and fabricated by using coating techniques (i.e., sol-gel, hydrothermal) that require a separate annealing process to promote crystallization. However, the requirement of high annealing temperature of these techniques often results in the cracking and failure of the produced coating due to the difference in thermal expansion during the annealing process. Hence, to overcome this limitation, the PEO method will be utilized throughout this research. PEO is an advanced coating technique used to grow porous ceramic layers on light metals that do not require a separate heat treatment step and is observed to effectively enhance mechanical integrity and adhesion. Examination of the physical appearance of the produced coating under FESEM and chemical analysis with EDX will suggest the mechanism of nanotube formation. The physicochemical characterization (Wettability testing, microhardness, adhesion analysis, and wear test) will be conducted to analyze the mechanical and tribological characteristics. The outcome on the uniformity of the growth will trigger further analysis on the bioactivity and compatibility of the coating as a medical implant in which to be continued in other project.
Objectives: | To identify the optimum PEO parameters on the homogeneity distribution of TiO2 nanotubes via optimization method To characterize the TiO2 nanotubes towards the possibility of application as a medical implant
Equipment required: | PEO set-up (AMMP lab), FESEM, EDS (Chemistry Dept.), Contact angle analysis,
Software required: | -
Supervisor (Department): | AP Datin Ir. Dr. Bushroa Abdul Razak (Dep of Mechanical Eng)
Program: | Master of Mechanical Engineering (Manufacturing Process)
Duration: | Maximum 2 consecutive semesters